## Slide 1: A Framework for Systematic Evaluation and Exploration of Design Rules
Rani S. Ghaida* and Prof. Puneet Gupta
EE Dept., University of California, Los Angeles
(rani@ee.ucla.edu), (puneet@ee.ucla.edu)
Work partly supported by IMPACT, SRC, and NSF.
<number>

## Slide 2: Motivation
Industry is faced with many technology options for scaling to every next node
DRs being the biggest design-relevant quality metric for a technology
  Evaluating DRs is absolutely necessary to decide on technology choices
Automated and systematic cell-level DR evaluator
  focus on early evaluation of layout-methodologies and DRs before exact process and design technologies are known
  avoid explicit simulation or excessive reliance on accurate models
<number>
Notes: <number>

## Slide 3: Overview of DR Evaluator
Fast layout estimation ← Fast topology generation + congestion estimation
<number>
Ongoing
This work
Notes: <number>

## Slide 4: Assumptions and Flow
CMOS circuits with dual transistors, multiple outputs, any transistor size, 1D transistor placement, i.e. on same row
Intra-cell routing in poly and M1 layers only (M2 ongoing)
PMOS
NMOS
Transistor chain
Transistor stack
Large
transistor
Folded
transistor
Transistor
pair
1D placement
<number>
Pairing
Folding
Chaining/Stacking
Transistor/
chain
ordering
Notes: <number>

## Slide 5: Example – Pairing
OAI211_X4 Netlist
<number>
Matching problem solved optimally with Hungarian algorithm
p2
p3
p1
D
D
C
C
A
B
A
B
n2
n3
n4
n1
Zn
Zn
Zn
N
N
N
ZN
 | TN1 | TN2 | TN3 | TN4 | TN5 | TN6
TP1 | 5.9 | 1.4 | 0 | 0 | 0 | 0
TP2 | 0 | 5 | 0 | 0 | 0 | 0
TP3 | 1 | 1 | 4.9 | 0 | 0 | 0
TP4 | 1 | 1 | 0 | 5.6 | 0 | 0
TP5 | 0 | 0 | 0 | 0 | 6.6 | 1.1
TP6 | 0 | 0 | 0 | 0 | 0.7 | 6.2
Pair
Pairing score table

## Slide 6: Example – Folding
Given fixed cell height (as a rule), exhaustive search to find optimal p/n transistor folding sizes.
Transistor pairs with a larger height are then folded into multiple pairs
<number>
Large
transistor
pair
Folded
transistor
pair

## Slide 7: Example – Chaining
OAI211_X4 Netlist
BIPARTITE GRAPH
<number>
C
D
D
A
B
Zn
N1
N2
A
B
C
C
D
A
B
B
Zn
N1
N2
C
D
A
p1
p2
p3
n1
n2
n3
n4
N folded
into N1/N2
Vertices → nodes in netlist and contain pairs the node connects to
Edges → possible diffusion sharing between pairs
  If large # of folds, cluster into groups and treat each as single pair
Chaining: find maximum set of compatible edges
p2
p3
p1
D
D
C
C
A
B
A
B
n2
n3
n4
n1
Zn
Zn
Zn
N
N
N
ZN
Chain
Stack

## Slide 8: Example – Chaining and Ordering
OPTIMAL ABUTMENT
LAYOUT
2 chains/2 stacks
<number>
ORDERING
FLIPPING
Chaining/Stacking:
  Edges are sorted according to upper bound
  on the number of abutment after selection
  Construct solutions in depth-first search with tree pruning
    Only need to examine first several solutions to find optimal in most cases
Chain ordering:
  Min cut placement of chains with exhaustive search for small # of chains
  For large # of chains, partition with FM algorithm and run exhaustive search to order partitions and chains within partitions
  Chains are possibly flipped to minimize WL
C. Hwang et al., TCAD 1990
A
B
D
C
Zn
N1
N2

## Slide 9: Routing and Congestion Estimation
M1 wiring for S/D-to-S/D and gate connections that cannot be on poly using single-trunk Steiner tree
  horizontal trunk in center of cell
Estimate congestion of vertical/horizontal tracks based on wire length and blockage by wires in orthogonal direction
  C = Occupied Track-Length / Available TL
  = (WL + Blocked TL) / Available TL
  Blocked TL = BlockageActual + BlockageOrthog
<number>

## Slide 10: M1 Area Estimation
If → increase cell-area to accommodate M1 wiring
Cth captures routing efficiency, I/O pin accessing, and congestion:
α and β determined empirically from actual cells from previous generation or trial routes
γ is for I/O pin-access requirement and is specified by user
U is utilization w/o considering blockage from orthogonal wiring
When Ux ≈ 0, → 1 => Cth larger
When Ux ≈ Uy, → 0 => Cth smaller
<number>

## Slide 11: Validation of Area Estimation and Runtime
Layout of Nangate cell-library (104 cells) were estimated
  Area estimated with 2.4% error on average
  Runtime of evaluation procedure is 20 minutes real time on a 2GHz clock speed and 2MB cache processor
Easily parallelizable with no overhead since cell topology generation is independent
<number>

## Slide 12: Evaluation of Manufacturability
Probability of survival (POS) from:
  Overlay of Poly/M1/Active to contacts and poly-to-active (normal distribution)
  Contact-hole failures
  Particle defects: place wires on equally spaced tracks, use a compact model for CAA for M1/poly/contact shorts/opens and gate-to-contact shorts. Example for M1/poly wires:
Vertical wires
Horizontal wires
<number>

## Slide 13: Evaluation of Variability
We consider the sources:
  diffusion and poly imperfections under average overlay error and line-end pullback (corner-rounding, line-end tapering)
  CD variability (using distribution)
Variability index is the total
change in drive current
where i is the source of variability
<number>

## Slide 14: Experimental Setup
45nm FreePDK and 65nm process from a commercial vendor
Benchmark designs varying from 4K to 43K cells synthesized using Nangate 45nm Open Cell Lib (scaled for 65nm testing)
POS values normalized to a 10x10mm chip-area
Baseline experiment with:
  1D-poly (non-fixed pitch)
  M1 power-straps
  9-track cell-height
<number>

## Slide 15: Evaluation of Poly-Restrictions
2D vs. 1D-poly
  Almost identical cell-area due to pairing and small overhead for gate-alignment according to FreePDK DRs
  32% less variability with 1D-poly
Fixed vs. non-fixed pitch 1D-poly
  23% less variability
  5% area overhead because min = contacted gate pitch
<number>
Notes:   Almost identical results for limited/2D-poly (U/W-shapes not beneficial)
Higher area overhead for fixed pitch if min gate pitch ≠ contacted pitch
<number>

## Slide 16: Evaluation of Power-Strap Styles
7% area overhead with diff straps (not true for small cell-height)
  Specific to FreePDK, opposite results for 65nm commercial process
84% larger variability with diff-power straps
  diffusion-rounding is dominant in tested cells
Manufacturability benefits of diffusion power straps:
  Gate-to-contact shorts are reduced
  Contact redundancy for power connections on power rail (no cost)
<number>
Notes: For small cell-height (7 tracks), diffusion power-straps lead to 5.8% area improvement because it reduces M1-congestion which affects area seriously in this case
<number>

## Slide 17: Evaluation of Cell-Height
Minor effect of cell-height decision on variability
    poly rounding and line-end tapering affected by cell-height decision are second-order sources of variability
In general, smaller cell-height  smaller area,
  Not true for (large) cells in high-performance designs
<number>

## Slide 18: Comparison of DRs from Different Processes
Compare DRs of std and LP 65nm process from same vendor with diffusion/M1 power-strap style and 1D-poly patterning
  LP better in terms of variability and manufacturability, but std process is more area-efficient (7.9% less area)
<number>
Notes:   diffusion power-straps lead to 5.2%/4.2% smaller cell-area (contrary to previous study with 45nm FreePDK) due to
    reduced M1-congestion
    reduced gate-spacing according to DR values of 65nm commercial process
<number>

## Slide 19: Exploration of Gate-Spacing Rules
Consider gate-to-diffusion (GD) and gate-to-contact (GC) rules in 65nm process and use diff power-straps and 1D-poly styles
  Solution corresponding to process GD/GC actual values falls very near the Pareto optimal frontier
    example shows the fidelity of our evaluation metrics and approach
<number>

## Slide 20: Summary
Flexible framework for:
  Early co-evaluation of technologies, DRs, and cell library architectures before exact process and design technologies are known
  Compare DRs from different processes
  Can be used in DR optimization loops to narrow down on reasonable DR choices
C++ source code available for download at http://nanocad.ee.ucla.edu/Main/Projects
<number>

## Slide 21: Future Work
Address DR effects on other layout characteristics including performance, power, and some notion of designability
Introduce a 2D printability model (not based on field simulation)
Extrapolate DR evaluation to the chip level and include intermediate and global metal/via layers
Study interactions and tradeoffs of variability and area
<number>
Evaluation at cell-level
Evaluation at chip-level

## Slide 22: Thank you!
Questions?
<number>

## Slide 23: Backup Slides
<number>

## Slide 24: Runtime Improvement in Chaining
Problem: Runtime for cells with trans folded into large # of folds
Special case for inverters/buffers
  Detect them based on connectivity info in netlist
  Force chaining of fingers of folded trans
  Give preference to sharing output signal so that power signal is at the edge allowing its sharing with other transistors
  Runtime improvement at no overhead
If trans is folded into large # of fingers (user-specified)
  Group fingers into multiple groups (user-specified)
  Treat each group as a single pair during chaining
  Unfold finger groups after chaining is complete
  Runtime improvement at negligible overhead
<number>

## Slide 25: Runtime Improvement in Chain-Ordering
Problem:
  Runtime of chain-ordering with exhaustive search in cells with large # of chains
Let user specify limit on # of chains for exhaustive search (Lim)
For cells with # of chains > Lim:
  Partition chains into groups with # of chains ≤ Lim using FM algorithm to minimize connection cuts between partitions
  Exhaustive search to order partitions
  Exhaustive search to order chains within each partition separately while taking the order of partition into account
<number>

## Slide 26: M1-Congestion Estimation
Estimate congestion of vertical/horizontal tracks based on wire length and blockage by wires in orthogonal direction
  C = Occupied Track-Length / Available TL
  = (WL + Blocked TL) / Available TL
  Blocked TL = BlockageActual + BlockageOrthog
Example of L-bend with tip facing
outer corner:
  (1) and (2) are actually blocked
  (3) effectively increases
  wirelength in orthogonal
  direction
<number>

## Slide 27: Outcomes Depend on Set of DRs
Power connection with M1
Power connection with diffusion
Have to increase cell-width to next allowable pitch
35 nm
90 nm
160 nm
140 nm
<number>
Special characteristics of FreePDK DRs, e.g.:
  Too small gate-to-contact spacing => huge effect on POS results for case of redundant contacts
  Large area overhead for fixed gate-pitch with diffusion power connection
Contacted pitch = min pitch

## Slide 28: UCLA_DRE Supported Rules
Layout styles
  Poly patterning (2D/limited/1D/fixed-pitch)
  Power-straps (Metal/Active)
DRs
  Poly: LEE, LEG, gate-to-CA, gate-to-active, gate-pitch, etc…
  Active: spacing, min width, extension beyond gate, etc...
  CA: width, spacing, poly/active enclosure, CA to active, etc...
  M1: width, 2D-spacing rules, overhang rules
  M2/Via1 (ongoing): width, 2D-spacing rules
  Mx in chip-level evaluation (ongoing)
  Well (ongoing): active-to-well edge
<number>